## Slide 1: MODULE II
ENVIRONMENTAL POLLUTION

## Slide 2: WATER POLLUTION
WATER POLLUTION
It may be defined as “the alteration in physical, chemical and biological characteristics of water which may cause harmful effects on human and aquatic life.
Types of Water Pollutants
The various types of pollutants can be broadly put under the following types:
(i) Sewage Pollutants (Domestic and Municipal Waste)
(ii) Industrial Pollutants
(iii) Agricultural Pollutants
(iv) Radioactive and Thermal Pollutants.

## Slide 3: WATER POLLUTION
Types of Water Pollutants
Domestic and Municipal Pollutants:
The sewage contains garbage, soaps, detergents, waste food and human excreta and is the single largest sources of water pollution.
Pathogenic (disease causing) microorganisms (bacteria, fungi, protozoa, algae) enter the water system through sewage making it infected.
Water polluted by sewage may carry certain other bacteria and viruses cannot grow by themselves, but reproduce in the cells of host organisms.
Typhoid, cholera, gastroenteritis and dysentery are commonly caused by drinking infected water.

## Slide 4: WATER POLLUTION
Types of Water Pollutants
(ii) Industrial Pollutants:
Industries are located near rivers or fresh water streams are responsible for discharging their untreated effluents into rivers like highly toxic heavy metals such as chromium, arsenic, lead, mercury, etc. along with hazardous organic and inorganic wastes (e.g., acids, alkalies, cyanides, chlorides, etc.).
Factories manufacturing plastic, caustic soda and some fungicides and pesticides release mercury (a heavy metal) along with other effluents in nearby water body.
Mercury enters the food chain through bacteria, algae, fish and finally into the human body. The toxicity of mercury became evident by the Minamata Bay tragedy in Japan during the period 1953-60.

## Slide 5: WATER POLLUTION
Types of Water Pollutants
(iii) Agricultural Waste: Manure, fertilizers, pesticides, wastes form farms, slaughterhouse, poultry farms, salts and silt are drained as run-off from agricultural lands.
The water body receiving large quantities of fertilizers (phosphates and nitrates or manures becomes rich in nutrients which leads to eutrophication and consequent depletion of dissolved oxygen.
Pesticides (DDT, dieldrin, aldrin, malathion, carbaryl etc.) are used to kill insect and rodent pests. Toxic pesticide residues enter the human body through drinking water or through food chain. These compounds have low solubility in water but are highly soluble in fats. .

## Slide 6: WATER POLLUTION
Types of Water Pollutants
(iv) Physical Pollutants
(a) Radioactive Wastes : found in water are radium and potassium-40. These isotopes originate from natural sources due to leaching from minerals. Water bodies are also polluted by accidental leakage of waste material from uranium and thorium mines, nuclear power plants and industries.
(b) Thermal Sources: Various industries, nuclear power plants and thermal plants require water for cooling and the resultant hot water is often discharged into rivers or lakes. This results in thermal pollution and leads to the imbalance in the ecology of the water body.

## Slide 7: WATER POLLUTION
Types of Water Pollutants
(iv) Physical Pollutants
(c) Sediments : Soil particles carried to streams, lakes or oceans form the sediments. The sediment become polluting due to their large amount. The sediments may damage the water body by introducing a large amount of nutrient matter.
(v) Petroleum Products: Crude oil and other related products generally get into water by accidental spillage from ships, tankers, pipelines etc. Besides these accidental spills, oil refineries, oil exploration sites and automobile service centres pollute different water bodies.

## Slide 8: WATER POLLUTION
Sources of Water Pollutants
Point and Non Point Sources of Water Pollution
When pollutants enter a stream, river or lake these gives rise to surface water pollution.
The surface water pollution has a number of sources. These can be categorized as:
a. Point and Non-point Sources
b. Natural and Anthropogenic Sources

## Slide 9: WATER POLLUTION
Sources of Water Pollutants
(i) Point and Non-point Sources
The well-defined sources that emits pollutants or effluents directly into different water bodies of fresh water are called point sources.
Domestic and industrial waste are examples of this type. The point sources of pollution can be effectively checked. On the other hand, the non-point sources of water pollution are scattered or spread over large areas.
(ii) Natural and Anthropogenic Sources
An increase in the concentration of naturally occurring substances is also termed pollution. The sources of such an increase are called natural sources. Siltation (which includes soil, sand and mineral particles) is one such natural source.

## Slide 10: WATER POLLUTION
Sources of Water Pollutants
(ii) Natural and Anthropogenic Sources
It is a common natural phenomenon, which occurs in most water bodies. Indiscriminate deforestation makes soil loose and flood waters bring silt from mountains into streams, rivers and lakes.
On the other hand, the human activities that result into the pollution of water are called anthropogenic or man -made sources of water pollution.
For example, domestic (sewage and waste water), industrial and agricultural wastes that goes into the rivers, lakes, streams and seas are anthropogenic sources. Certain materials that are leached from the land by run-off water and enter the various water bodies also belong to this category
.