## Slide 5: ANALYSIS OF TRUSS BY METHOD OF SECTIONS

## Slide 8
FBD (take moment about point E)
FCE (take moment about point B)
FBE (ΣFy= 0)

## Slide 9: VA = 72.5 kN VD = 77.5 kN
D
E
A
40 kN
50 kN
60 kN
B
C

## Slide 10: VA = 72.5 kN VD = 77.5 kN
D
E
A
40 kN
50 kN
60 kN
B
C
x
x

## Slide 11
40 kN
E
A
B
FBE
FBC
FAE
VA = 72.5 kN
FAE (take moment about point B)
FBE (ΣFy= 0)
FBC (take moment about point E)

## Slide 12
40 kN
E
A
B
FBE
FBC
FAE
VA = 72.5 kN
(ΣFy= 0)
72.5 – 40 – FBEcos30 ° = 0
FBE = 37.57 kN (tension)
FAE (take moment about point B)
(ΣMB= 0)
(72.5 x 1.5) – (FAE x2.59) = 0
FAE = 41.98 kN(tension)

## Slide 13
40 kN
E
A
B
FBE
FBC
FAE
VA = 72.5 kN
FBC (take moment about point E)
(ΣME= 0)
(72.5 x 3) – (40 x 1.5) + (FBC x2.59) = 0
FBC = – 60.81 kN(Change the direction of arrow)
FBC = 60.81 kN (compressive)

## Slide 14
The following table list the forces, the magnitude and nature of the forces.
Sr. No. | Member | Force (kN) | Nature
1 | AB | 83.71 | COMPRESSIVE
2 | BC | 60.61 | COMPRESSIVE
3 | CD | 89.48 | COMPRESSIVE
4 | ED | 44.74 | TENSILE
5 | DC | 31.75 | TENSILE
6 | BE | 37.52 | TENSILE
7 | AE | 41.85 | TENSILE

## Slide 15
Determine the force in the member BD and DE.

## Slide 16
Based on a free-body diagram of the entire truss, solve the 3 equilibrium equations for the reactions at E and C.

## Slide 17
Joint A is subjected to only two unknown member forces. Determine these from the joint equilibrium requirements.
There are now only two unknown member forces at joint D.

## Slide 18
There are now only two unknown member forces at joint B. Assume both are in tension.
There is one unknown member force at joint E. Assume the member is in tension.

## Slide 19
All member forces and support reactions are known at joint C. However, the joint equilibrium requirements may be applied to check the results.

## Slide 21
Determine the force in members CD and DF of the truss
shown.

## Slide 22
Determine the force in members DG and FI of the truss shown

## Slide 23
Determine the force in members GJ and IK of the truss shown

## Slide 25
Determine the force in members EH and GI of the truss shown